## Slide 1: UA Object Serialization
PNO OPC UA JWG Proposal
2022
© PNO OPC JWG

## Slide 2: Motivation I - Sample: Config Object from Encoder Spec

## Slide 3: Motivation II - Config Variable with Structure Data Type

## Slide 4: Proposal PubSub - Generic Generated Structured Variable Steps when adding an Object to published DataSet
Automatically …
Create temporary data type representing the submodel of the object
Add this data type to the DataSetMetaData utilizing generic DataType ID
Add variable with the BrowseName of the object and the previously generated DataType (step 1, referenced by generic DataType ID step 2) to the published DataSet

## Slide 5: Proposal: General Value for Objects representing the Submodel of the Object as custom DataType
Automatically …
Create temporary data type representing the submodel*) of the object
Extend NodeClass for Objects with a Value Attribute
Add DataType definition reference for temporary data type (Step 1) to each Node instance
  New „HasDataTypeDefinition“ reference connects the Object instance to the temporary DataType definition node
Changes in the Object‘s Submodel will immediately result in a change of the temporary DataType definition
*) Means the object as root and all hierarchical referenced entities with the object as source in a recursively manner.
Enhancement M. Damm

## Slide 6: Enhancement M. Damm
To get rid of the additional DataTypeDefinition Node Matthias proposes:
The Value attribute consists of:
  DataType / ValueRank / ArrayDimensions
Change DataType Attribute to DataTypeDefinition Attribute at the ObjectType

## Slide 7: Proposal: Consequence for Reading or Subscribing
When reading or subscribing the Object, the Client will read / subscribe the Object‘s Value and the temporary data type definition
If a Value in the Submodel changes, the Object‘s Value will change. So the Object‘s Value will be published, but not the temporary DataType definition.
If the structure of the Submodel changes, the the Object‘s Value will change and also the temporary DataType definition. Both will be published.
For PubSub: If temporary DataType definition changes, the PubSub metadata changes also.